## Slide 1
SmartCar
An AI-Powered Autonomous Vehicle System
with Real-Time IoT Control
B.Tech Project Report
Submitted by
Pr4xh4r
Guide: [Guide Name]
[College Name]
2025 - 2026
Raspberry Pi 3 | Single Camera | Edge AI | IoT | Under INR 5,000

## Slide 2
Problem and Our Solution
The Problem
LiDAR sensors cost $5,000+
Computing units cost $10,000+
Proprietary closed-source software
Inaccessible for students and researchers
Our Solution
Raspberry Pi 3 (INR 2,500)
Single Pi Camera (INR 250)
Total cost under INR 5,000
100% open-source software
Edge AI with sub-100ms latency
SmartCar achieves SAE Level 2 autonomy at 0.1% the cost of commercial systems

## Slide 3
System Architecture and Hardware
User Interface
Web App | Telegram | Cloud
▼
Application
Flask + SocketIO | MQTT | Bot API
▼
AI / Vision
6 CV Modules (OpenCV)
▼
Control
GPIO + PWM | Camera | LED
▼
Hardware
RPi 3 | L298N | Motors | Camera
Raspberry Pi 3
1.2GHz Quad-Core
1GB RAM, WiFi, BT
Pi Camera v1.3
5MP, 1080p at 30fps
CSI Interface
L298N + 4 Motors
Dual H-Bridge Driver
Differential 4WD
Power System
Li-ion 7.4-12V
LM2596 Buck to 5.1V
Total BOM: INR 4,000 to 5,000 (approximately $60)

## Slide 4
6 Driving Modes + 6 AI Safety Features
Driving Modes
1
Manual Control
Web/Telegram real-time driving
2
Line Following
PID controller, black line tracking
3
Traffic Light
HSV segmentation (R/G/Y)
4
Auto Pilot
Line follow + traffic combined
5
Smart Parking
FSM-based, green marker detect
6
Convoy Mode
HSV color tracking + PD control
AI Safety Features
Collision Prediction
4-frame tracking + auto-brake + TTC
Pedestrian Detection
Frame diff + aspect ratio + direction
Accident Detection
3x baseline spike + SOS + 5 photos
Road Condition
Laplacian variance + speed adjust
Driver Behavior
Safety score 0-100 from commands
Convoy Tracking
Color-based follow with PD steering
All AI runs at the edge: ~7 FPS, sub-100ms latency, ~60-75% CPU, 400-500MB RAM

## Slide 5
IoT Integration and Test Results
Local WiFi
Latency:
<10ms
Protocol:
Flask + SocketIO
Internet:
Not needed
Telegram Bot
Latency:
100-300ms
Protocol:
Telegram API
Internet:
Required
MQTT Cloud
Latency:
50-200ms
Protocol:
MQTT over WSS
Internet:
Required
Test Results: All 13 Tests Passed
10 FPS
Camera
~7 FPS
AI Processing
~85%
Collision Accuracy
~90%
Traffic Light Accuracy
~30s
Boot Time
MQTT topics enable real-time command, speed, mode, camera stream, and status updates

## Slide 6
Conclusion and Future Scope
Key Achievements
6 driving modes + 6 AI features on RPi 3
Edge AI at ~7 FPS, sub-100ms latency
3 control channels (WiFi, Telegram, MQTT)
Automatic accident SOS with photo evidence
Total cost under INR 5,000 (0.1% of Tesla)
Future Scope
GPS module for location tracking
Ultrasonic sensors for distance
TensorFlow Lite for better detection
V2V communication via MQTT
SLAM for map-free navigation
Fleet management dashboard
"SmartCar proves that intelligent vehicle systems can be democratized
through edge computing and open-source software."

## Slide 7
Thank You!
Presented by
Prakhar Sharma
23EEAEC034
Vidhi Jangid
23EEAEC027
SmartCar - AI-Powered Autonomous Vehicle System | B.Tech Project | 2025-2026